Pavendar Bharathidasan College of Engineering & Technology

Thanjai Natarajan Nagar, Mathur, Trichy 620 024

# MODEL TEST

ME 6253 – Finite Element Analysis  / Mechanical Engineering Department                                                                       Date / Session: 28.032015                                                            Time: 9.30  – 12.30  A.M                            	   Year/ Sem:  III / VI         PART – A (10 x 2 = 20 marks)          Max Marks: 100

- What are the types of boundary conditions ?

- What are the characteristics of shape function ?

- What are 'h' and 'p' versions of Finite Element method ?

- What is the necessity for Isoparametric element analysis ?

- What is meant by plane stress analysis ?

- Write down expression of stiffness matrix for a truss element axial vibration of one dimensional rod?

- What are the governing differential equation for one dimensional heat equation ?

- What are the ways in which fluids are classified ?

- What are the different modes of heat transfer ?

- Define thermal conductivity and convection heat transfer co-efficient

PART – B (16 x 5 = 80 marks)

1 a )  The differential equation of a physical phenomenon is given by d2y / dx2  + y = 4x  ,  0 <= x  >= 1  The boundary conditions are y(0) = 0 and  y(1) = 1  Obtain  one term approximate solution by using Galerkin’s method of  Weighted  residuals.    E = Young’s modulus    ,  A = Cross sectional area

b) A bar o uniform cross section is clamped at one end and left free at the other end and it is subjected to a uniform axial load P . Calculate displacement and stress in a bar by using two terms polynomial and three terms polynomial and compare with exact solution.

2. a) Derive one dimensional bare element Finite element analysis and Assemble the stiffness equation or global equation for bar equally divided into four element.

b) Solve the problem explained by dividing the bar into 4 equal parts.

3  a) Explain Constant strain Triangle ?  Derive the shape function for the constant strain triangle ?

- A thin plate is subjected to surface traction .Calculate the Nodal displacement for element 1 and element 2 and Global stiffness matrix.

4. a) Determine the natural frequency of vibration for a beam fixed at both ends. The beam has mass density (, modulus of elasticity E , cross section A , moment of inertia I , and length 2 L , For simplicity of the long hand calculation , beam is discretized  into two element of Length L..

b)  For axial motion of a rod and for the transverse motion of the beam how the Striffness matrix equation of beams  or rods based on Lagrange’s method  of equation for motion used taken T as kinetic energy and ( as potential energy in the generalized coordinates. Find the formulation of finite element equation.

5. a) Write about Fluid Flow Mechanism  and  Derive the Shape function for Two dimensional  Element  for an Fluid  Flow ?

b) 1 For a smooth pipe of variable cross –section determine the potential at the junctions. The potential at the let end is p1=10m and that at right end is p4 = 1m. If the velocity of fluid at the left end is 1.5 s/m. Find the velocities at the junctions and right end. Also determine the volumetric flow rates.

Pavendar Bharathidasan College of Engineering & Technology

Thanjai Natarajan Nagar, Mathur, Trichy 620 024

# MODEL TEST

ME 6253 – Finite Element Analysis /  Mechanical Engineering Department                                                                    Date / Session: 28.032015                                                                      Time: 9.30  – 12.30  A.M               Year/ Sem:  III / VI                                 PART – A (10 x 2 = 20 marks)                               Max Marks: 100

- What is the different between Static and Dynamic Analysis ?

- What is meant by Finite Element Analysis?

- What is Rayleigh-Ritz method?

- Differentiate Global axis and local axis

- Define super parametric element ?

- What are the conditions for a problem to be axisymmetric.

- Write down the stress-strain relationship matrix for plane stress condition.

- Write equation for steady state heat transfer and explain

- What are the ways in which fluids are classified ?

- Drive the shape function for two dimensional heat transfer element.

1.  a) A  Simply supported  beam subjected uniformly  distributed load over entire span  and it is subjected to a point load on the center of  the span. Calculate the bending movement and deflection at mid span by using  Rayleigh-Ritz method and compare with exact solution.

b) Define finite element Analysis and explain all the analytical methods and explain Element, Discritization, node and nodal points and shape function.

2 . a) A thin steel plate of uniform thickness 25mm is subjected to a point load of 420 N at mid depth .The plate is also subjected to self-weight. If Young’s modulus E= 2 x10-4mm / N3.  Calculate the displacement at each nodal point, Stress in each element

.

b) A two nodded truss element the given nodal displacement are U1-5mm  and U2 = 8mm . Calculate displacement at x = l/4 , l//3 , and  l/2.

3. 1) Determine the stiffness matrix for the constant strain triangular element The co ordinates are given in units of millimeters Assuming plane stress conditions  and take E = 210GPa, v=0.25 , t= 10mm

b)  Establish the strain displacement matrix for the linear quadrilateral element  at  gauzz point  rr = 0.57735 and s = -0.57735.

4. a) Find the natural frequency of longitudinal vibration of the unconstrained stepped bare

b) For an un dumped  2 degree of freedom system find the respond of the system when first mass alone is given an initial displacement of unity and released from rest

. 5. a) Drive Stiffness Matrix and Lo ad Vector for Heat Transfer in Two-dimensional Element (Triangular element

b)Compute the element matrix and vectors for the element shown is figure when the edges 2-3 and 301 experience convection heat loss

# Text boxes

m

m